# Raspberry Pi & Arduino
While there are many I/O boards under development for the Raspberry Pi, the Arduino is well established, and is much easier to replace if you accidentally fry it. This article shows you how talk to an Arduino through Python and the Firmata protocol.
Firmata (http://firmata.org) is a simple serial protocol that allows you to read and write I/O ports on the Arduino from a host computer. It's most often used with the graphical programming language Processing (http://processing.org) but there is support for other languages. This example combines output (setting the brightness of an LED with a graphical slider) with input (reading the temperature from an LM58).
## Installing the Arduino IDE and Firmata
The Arduino IDE is already included in the Raspbian repositories, so you can install it all with:
sudo apt-get install arduino
If it's the first time you've run it, the IDE may ask you to create a folder for its programs (called “sketches”).
Next, you'll have to choose what Arduino board you're using from the Tools/Board menu (I'm using an Uno, but I've tested this on an older Duemilanove board too). You'll also need to choose which serial port to use from Tools/Serial Port — for an Uno that would be /dev/ttyACM0, and older boards tend to use /dev/ttyUSB0.
To install the Firmata sketch onto your Arduino, select File/Examples/Firmata/StandardFirmata and click the Upload button. The IDE goes off and compiles your sketch, and uploads it. If all you get is blinking lights and a ‘Done uploading’ message, success! If you get any kind of red error messages, then there's likely something up with the connection or power to the Arduino. I'd strongly recommend connecting your Arduino either through a powered hub or applying external power, as the Raspberry Pi is a bit limited in what it can power over USB.
## Installing pyFirmata
pyFirmata is the magic that allows your Arduino running Firmata to talk to Python. It takes a few more commands to install it:
sudo apt-get install python-serial mercurial
hg clone https://bitbucket.org/tino/pyfirmata
cd pyfirmata
sudo python setup.py install
If this succeeds, you can remove the pyfirmata folder (cd .. ; sudo rm -r pyfirmata).
## Building the Circuit
Parts list:
- Arduino board
- small solder-less breadboard
- LM35 temperature sensor (http://www.ti.com/product/lm35)
- 5 mm red LED
- 120 Ω resistor
- 4× male-male jumper wires (here coloured red, yellow, blue and black)
- short-ish breadboard jumper (17.8 mm or 0.7", here coloured black)
Place the parts as shown in the diagram:
1. Connect the LM35: +Vs → Arduino +5V, Vout → Arduino pin A0, and GND → Arduino GND
   (If you accidentally connect the LM35 the wrong way round, it goes from being a temperature sensor to being a remarkable temperature generator — the D-shaped burn scar on my left index finger reminds me of this every day…)
2. Connect the LED: anode (long wire) → Arduino pin D3, cathode (short wire, flat side) through the 120 Ω resistor to Arduino GND.
## Running the code
With your Arduino plugged in, and the circuit wired up, you run the program like this:
python arduino_firmata_tk.py
It will take a few seconds for the window to come up, and once it does, you can control the LED's brightness with the slider on screen. The LED doesn't seem to get much brighter above 33%, you'll notice; there isn't a straight-line link between brightness and PWM input voltage. If you touch the LM35, you'll notice the temperature reading changing. LM35 sensors are a bit noisy, so you might notice the numbers jumping about. Once you're done, hit the window close widget, and everything should exit cleanly.
The Python code does three main tasks:
1. Set up serial communications and configure the Arduino's I/O pins. Two important details we have to do here is set up an iterator thread to stop the Raspberry Pi's serial buffer overflowing while it receives data from the Arduino, and also to wait for the Arduino to start sending real data before we move on to the main program.
2. Define three functions to be called by the GUI:
- get_temp() — this reads the value from Arduino pin A0, converts it to °C, and updates the label at the bottom of the window. If you're familiar with Arduino, pyFirmata returns analogue values between 0.0 and 1.0 instead of the integer range 0-1023. This routine ends by asking the main Tk process to reschedule itself after half a second (500 ms), and that way we keep updating the temperature display separate from the main loop.
- set_brightness() — this converts the 0-100 value from the GUI's Scale slider widget to a 0.0-1.0 floating point range, and writes it to pin D3.
- cleanup() — all this routine does is turn the LED off, and tries to shut down the program neatly. It doesn't always quite manage to do this, however; sometimes you have to hit Ctrl-C in the terminal window too.
Set up the Tkinter GUI. Tk (and its Python version, Tkinter) is quite an old GUI system, but is also quite simple to use. It relies on each widget (or graphical control) to run a callback routine or set a variable's value as it is clicked or changed. So here, I'm setting up a 400 pixel wide Scale slider that calls the routine set_brightness() with the current value of the slider as it changes. Moved fully to the right, the slide would call set_brightness(100), turning the LED fully on. Since the window is so simple – just one Scale widget and a label — I'm using Tk's crude pack() method to arrange items in the window. It first draws the items, then packs them together, Tetris-like, into the window frame. Once it's done that, it schedules the first temperature reading (which schedules the next, and so on), then finally sits in the Tk mainloop() for the rest of the program, responding to your input.
## Further directions
This is a very simple example of controlling an Arduino from Python. While Firmata can control more complex outputs such as servos, it does take over the whole logic processing of the Arduino board. Any sensor that requires complex setup or real-time control isn't going to work so well. That aside, you've now got all the power of the Raspberry Pi hooked up to the simple robustness of the Arduino; the sky's not even the limit!

Article by Stewart C. Russell
Stewart C. Russell lives in Toronto, where he engineers wind farms and solar power plants. When he's not lurking in the world's sunny/windy places, he's at home on amateur radio (call sign VA3PID), playing banjo, fiddling with computers, or avoiding gardening. His website is http://scruss.com/blog